## Slide 1
HD HYUNDAI ELECTRIC
Circuit Breaker

## Slide 2
Overview & Plan

## Slide 3: [Product OVERVIEW(HDHE)]
Energy solution
MV/LV Switchgear
MV/LV Circuit breaker
& Contactor
Motor/Generator
Power Transformer
Gas Insulated Switchgear

## Slide 4: [Product OVERVIEW(MLV CURCUIT BREAKER) ]

## Slide 5: [Power Distribution Product Certification Status(~2025)]
(Oct. 25)
(Oct. 25th)
(May. 24)
(~Apr. 26)
(~Feb. 26)
(~Mar. 26)
(Stp. 25th)
(May. 14)
(May. 20)
Notes: As mentioned by our sales team, I would like to provide an update on the current status of UL-certified products.
As of today, we have successfully obtained UL certifications for key products, including medium-voltage circuit breakers and low-voltage devices, to supply to the U.S. market.
To expand the U.S market, we developed low-voltage circuit breakers such as MCCB, ACB, and MS. With great support from UL, we obtained certification and launched these products at the end of last year.
Regarding C-GIS and E-GIS, development started in 2023, and certification testing has been completed. We expect to receive the official UL certificate early this year.

## Slide 6
UL Products
UL MC & TOR
Digital Motor Protection Relay
UL MCCB
UL ACB
UL VCB & VI
UL VCS

## Slide 7: 1. UL MC
Notes: 22B 제품/인증은 있는데 -> Havells 제품이라 생산처 이슈로 제외 검토

## Slide 8: 1. UL MC & TOR
Product Characteristics

## Slide 9: 1. UL MC & TOR
Ratings and Specifications
Notes: 9/12/18/22B 제품/인증은 있는데 -> Havells 제품이라 생산처 이슈로 제외 검토

## Slide 10: 1. UL MC & TOR
External Structure

## Slide 11: 1. UL MC & TOR
Product Features

## Slide 12: 1. UL MC & TOR
Accessories

## Slide 13: 2. Digital Motor Protection Relay (HGMP)

## Slide 14: 2. Digital Motor Protection Relay (HGMP)
Overview and Characteristics

## Slide 15: 2. Digital Motor Protection Relay (HGMP)
Ratings and Specifications

## Slide 16: 2. Digital Motor Protection Relay (HGMP)
External Structure

## Slide 17: 2. Digital Motor Protection Relay (HGMP)
Model |  | N60 |  |  | A60 |  | P1001)
 |  | I | Z | B | Z | B | Under develop
Protection Type | Current | ● | ● | ● | ● | ● | ●
 | Voltage | - | - | - | - | - | ●
 | Power | - | - | - | - | - | ●
Protection functions | Over | ● | ● | ● | ● | ● | ●
 | Under | ● | ● | ● | ● | ● | ●
 | Phase failure | ● | ● | ● | ● | ● | ●
 | Phase Imbalance | ● | ● | ● | ● | ● | ●
 | Rotor – Stall | ● | ● | ● | ● | ● | ●
 | Rotor – Lock | ● | ● | ● | ● | ● | ●
 | Reverse phase | ● | ● | ● | ● | ● | ●
 | Earth leakage | ● | - | - | ● | ● | ●
 | Ground fault | ● | ● | ● | ● | ● | ●
 | Instantaneous | - | ● | ● | ● | ● | ●
Display information | Real-time load current | ● | ● | ● | ● | ● | ●
 | Real-time load rate | ● | ● | ● | ● | ● | ●
 | Check parameters during operation | ● | ● | ● | ● | ● | ●
 | Check total running | ● | ● | ● | ● | ● | ●
Comm. protocl | RS – 485 / Modbus | - | - | - | ● | ● | ●
 | Ethernet | - | - | - | - | - | ●
Ects | Contact | Main : 3ea | Main : 2ea Aux : 1ea | Main : 2ea Aux : 1ea | Main : 3ea | Main : 3ea | Main : 5ea Aux : 3 ea
 | Built-in ZCT | - | - | ● | - | ● | ●
Electric Motor Protection Relay(HGMP) LINE-UP
As this is a product under development, some specifications may change.
And motor control function will be supported in the future.

## Slide 18: 2. Digital Motor Protection Relay (HGMP)
Communication Function(Advanced Type)
Supports the universal industrial communication protocol RS-485/Modbus to enable easy interfacing into the user’s integrated control network.
User can get the waveform of the lasts trip by Modbus protocol

## Slide 19: 2. Digital Motor Protection Relay (HGMP)
Installation
Main Part : Fixed by screw or DIN rail mount
[Screw type]
[DIN rail type]
Display Part : Fixed plate, rubber washer and screw included
[Main-Display connection cable]

## Slide 20: 2. Digital Motor Protection Relay (HGMP)
HGMP P100 (Under development)
Up to 100A rated current without external CT
Enhanced protection and monitoring for voltage and power
Network redundancy (Rapid Spanning Tree Protocol)
Motor preventive diagnostic system supports
Integrated CT & ZCT | Communication Option | Motor Control
Integrated 3phase CT module including ZCT for earth leakage protection Rated current : 0.5~100A ZCT measurement range: 30mA~10A | Modbus/RTU(RS485): 9600~57600bps Modbus/TCP(RJ45): 100Mbps, RSTP supports ※ RSTP(Rapid spanning Tree Protocol) network protocol that builds a loop-free logical topology for Ethernet networks. | HGMP P100 type: Power type/Control type - Control type has DI 4 channels and DO 2 channels to control the motor (I/O module)

## Slide 21: 2. UL MCCB
Overview – HD HYUNDAI ELECTRIC

## Slide 22: 2. UL MCCB
Product Characteristics
600Y/347Vac
65kA

## Slide 23: 2. UL MCCB
SPECIFICATION
65
65
65
65
120/240V

## Slide 24: 2. UL MCCB
External Structure
③
②
①
④
⑤
⑥
⑦

## Slide 25: 2. Frame Size : 125AF

## Slide 26: 2. Frame Size : 150/250AF

## Slide 27: 2. Frame Size : 400/600AF
13.39(340)

## Slide 28: 2. UL MCCB
Lug specification

## Slide 29: 2. UL MCCB
Accessories

## Slide 30: 2. UL MCCB
Accessories Detail

## Slide 31: 2. UL MCCB
Accessories Detail

## Slide 32: 2. UL MCCB
Accessories Detail

## Slide 33: 2. UL MCCB
Handle Accessories NEMA rating (UL 50E Cert.)
Lock out, Tag-out, Interlock, Door Release function

## Slide 34: 2. UL MCCB
HGU 150/250/400/600
HGU 125

## Slide 35: 3. UL ACB
Overview – HD HYUNDAI ELECTRIC

## Slide 36: 3. UL ACB
Overview
Rated Impulse Withstand Voltage : 1000V
100% N Phase Current Flow
Capacity for all Types
A Frame [635V : 65kA, 508V : 85kA ]
400 ~ 1600A (HGL)
B Frame [635V : 85kA, 508V : 100kA]
400 ~ 3200A (HGL)
C Frame [635V : 85kA, 508V : 100kA]
1600 ~ 4000A (HGL)
D Frame [635V : 100kA, 508V : 130kA]
2500 ~ 6000A (HGL)

## Slide 37: 3. UL ACB
SPECIFICATION – HD HYUNDAI ELECTRIC (Under developing, ~’25.06)

## Slide 38: 3. UL ACB
LAY-OUT
1,600AF
2,500AF
Front
Side
Bottom
Front
Side
Bottom

## Slide 39: 3. UL ACB
LAY-OUT
4,000AF
6,000AF
Front
Bottom
Front
Side
Bottom
Side

## Slide 40: 3. UL ACB
OCR
OCR/CT Rating Plug
Case

## Slide 41: 3. UL ACB
Ethernet Communication Option(under Development, ~26.12)
Modbus/TCP
Ethernet_IP
Modbus/RTU
Modbus/RTU over Ethernet
Dual Port LAN : 10/100Mpbs
Mounting on DIN rail
Supporting Ethernet protocols
- Modbus TCP (in development) - Ethernet IP (in planning)
- Rapid Spanning Tree Protocol (RSTP) - Network Time Protocol (NTP)

## Slide 42: 3. UL ACB
Accessories

## Slide 43: 3. UL DC DSU(UL Certification in Process, ~May, 26)
Overview – HD HYUNDAI ELECTRIC

## Slide 44: 3. 개발제품 정격
3. UL DC (UL Certification in Process, ~May, 26)

## Slide 45: 4. UL VCB/VCS/VI

## Slide 46: 4. UL VCB/VCS/VI
Overview – VCB(Vacuum Circuit Breakers)
- Specification
1. Full line-up of high/middle/low VCB models.
1) 4.76kV 25kA 630-2,000A
2) 4.76kV 31.5/40kA 630-3,000A
3) 4.76kV 50kA 630-4,000A
4) 15kV 31.5/40kA 1,200-3,000A
5) 38kV 31.5/40kA 1,200-3,000A
2. Strong structure with high reliability.
1) High dielectric strength and temperature rising
2) Reliable mechanical durability
3) Excellent breaking capability
3. Convenience and Supply a variety of accessories.
1) Full types of Cradle
4. Certified by ANSI C37.09 and UL Recognized.

## Slide 47: 4. UL VCB/VCS/VI
Ratings and Specifications - VCB(Vacuum Circuit Breakers)

## Slide 48: 4. UL VCB/VCS/VI
Product Features - VCB(Vacuum Circuit Breakers)

## Slide 49: 4. UL VCB/VCS/VI
Type of Mounting - VCB(Vacuum Circuit Breakers)

## Slide 50: 4. UL VCB/VCS/VI
Accessories - VCB(Vacuum Circuit Breakers)

## Slide 51: 4. UL VCB/VCS/VI
Accessories - VCB(Vacuum Circuit Breakers)

## Slide 52: 4. UL VCB/VCS/VI
Accessories - VCB(Vacuum Circuit Breakers)
Draw in/out Accessories
Designation Accessories

## Slide 53: 4. UL VCB/VCS/VI
Overview & Specifications – VCS(Vacuum Circuit Switch)
Certificate
UL, cUL, (Standards by UL347, NEMA ICS 3)

## Slide 54: 4. UL VCB/VCS/VI
Overview & Specifications – VCS(Vacuum Circuit Switch)

## Slide 55: 4. UL VCB/VCS/VI
External Structure – VCS(Vacuum Circuit Switch)

## Slide 56: 4. UL VCB/VCS/VI
Cradle Selection – VCS(Vacuum Circuit Switch)

## Slide 57: 4. UL VCB/VCS/VI
Accessories – VCS(Vacuum Circuit Switch)

## Slide 58: 4. UL VCB/VCS/VI
Overview – VI(Vacuum Interrupter)

## Slide 59: 4. UL VCB/VCS/VI
Ratings and Specifications– VI(Vacuum Interrupter)

## Slide 60
Thank you for your attention !